## Slide 1: Project Objective
Correlate physical and digital events for total security
Focus on individual sensors which perform initial data collection
Hub device to relay sensor information to MAHIVE server
Modular system that can adapt to many situations or buildings

## Slide 2: Value Proposition
Hacking and attacks are ever increasing threat; industry needs way to protect physical/digital
MAHIVE project merges cyberphysical & cybersecurity solutions into one platform
Team TBD will create a hub controller that will:
  Link IoT devices
  Consolidate Reports into TRDF format
  Encrypt the data
  Securely send to MAHIVE server

## Slide 3: Product Requirements
Product must send messages in TRDF format
Messages must be encrypted
Product must authenticate itself (via PKI)

## Slide 4: Design Constraints
Design must be low-cost (goal for sensors: <$50)
  No elaborate, costly solutions
Design must use off-the-shelf parts/boards
  Raspberry Pi, etc.
  Use simple sensory parts readily available online
Sensors should be able to run off battery power
  Board should have low power consumption
  Interrupts rather than polling
Sensor device should be small & easily placed inside building

## Slide 5: Project Progress to Date
Decided on hardware to use
  Hub Device: Raspberry Pi 3
  Leaf devices: ESP32
Ordered Parts/devices
  ESP32
  Raspberry Pi
  Sensors/switches
  Breadboards, wires, etc.
  Battery Packs

## Slide 6: Project Progress (cont’d)
ESP32: flashed with Amazon FreeRTOS, running Greengrass Connectivity Demo
  Discovers local hub device
  Authenticates on AWS
  Sends MQTT message to AWS cloud via hub device
Raspberry Pi
  Running Greengrass Core software
  Deployed as hub device with potential for C/Python lambda functions
  Communicates directly with AWS cloud

## Slide 7: Remaining Project Schedule
After Spring Break: FreeRTOS modified sufficiently to utilize sensors on ESP32
End of March: Full working sensor relaying data in proper format to cloud, able to display on computer
Early April: Print Poster for project
End of April: Demo setup with 2X ESP32 door/light sensors, Pi hub, computer, etc. Finished & ready for expo

## Slide 8: Costs/Budget (Hub Device)
Raspberry Pi: $35
MicroSD card: $6
-------------------------
Total: $41

## Slide 9: Costs/Budget (Leaf)
ESP32: $11
Battery Pack: $10
Sensor: $5
Breadboard: $3
Total: $29

## Slide 10: Potential Issues/Risks
Possibility that learning/modifying FreeRTOS is too complicated/time consuming for scope of this project
  Could modify demo project for sake of proof-of-concept
Hard decision may have to be made between power consumption and reliability of sensors
  Sensor reliability more important
  If interrupts cannot be used, can implement polling and wall power instead
May not be able to learn how to format sensor data into TRDF format
  JSON may also be acceptable, but should not be too hard to implement TRDF